## Slide 1: Wireless Sensor Networks
Assignment 2
Packet propagation to all nodes
Μπαδάκης Ιωάννης 1590
Τσακίρης Τρύφων 1655

## Slide 2: Description
Best-effort network-wide broadcast
Requirements:
  Propagation with flooding
  Collision avoidance
  Steady silent state

## Slide 3: Design
Buffering
  on each node
  handle duplicates
  forward broadcasted packets
  cyclic storage
  max size of 10 slots
  save (node_id, seq_no)
  2 indexes (buff_indx, fwd_indx)
  1 counter for wrap arounds (carry)
Packet
  group id
  node id
  sequence number

## Slide 4: Design
Tasks
  broadcastMsg()
    set packets fields
    send it over the radio
    update local seq_no counter
  forwardMsg()
    set packets fields
    send it over the radio
    update fwd_indx counter
  bufferMsg()
    drops duplicate packets
    save non-duplicates
    schedule a transmission time

## Slide 5: Implementation
General Idea Pseudocode: (with omitted info)
event receive();
if not my_group: { return; }
post bufferMsg();
task bufferMsg():
if rcv_pkt in buffer: { return; }
saveTobuffer();
startTimer(); /* random backoff time */
event timer.fired();
post forwardMsg();
event sendDone();
If pkts_to_fwd: { startTimer(); }
void startTimer() {
uint16_t delay;
if(call Timer.isRunning()) {return; }
delay = call Random.rand16() % 50;
call Timer.startOneShot(delay);
}

## Slide 6
Example Carry brief explanation
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
carry++
assume buffer is full
fwd_indx
buff_indx
rcv_pkt
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
buff_indx
fwd_indx
Current state:
buff_indx = 9
fwd_indx = 6
carry = 0
Current state:
buff_indx = 0
fwd_indx = 6
carry = 1
if buff_indx == MAX_SIZE - 1 :
  buff_indx = 0 (wrap around)
  carry ++
if fwd_indx == MAX_SIZE - 1 :
  fwd_indx = 0 (wrap around)
  carry --

## Slide 7: Example Single node broadcast
0
1
2
3
4
[0,0]
buff_indx ++
seq_no ++
{}
{}
{}
{}
{}
buffer
rcv_pkt
Initial state:
buff_indx = 0;
fwd_indx = 0;
carry = 0
checkBuffer()
n
y
drop pkt
startTimer()
<0,0>

## Slide 8
0
1
2
3
4
{}
{}
{}
{}
{[0,0]}
event sendDone()
if(buff_indx > fwd_indx || carry != 0)
nothing to do!
n
y
startTimer()
Current state:
buff_indx = 0
fwd_indx = 0
carry = 0
Example Single node broadcast

## Slide 9
0
1
2
3
4
{}
{[0,0]}
{}
{}
{}
checkBuffer()
drop pkt
<0,0>
event Timer.fired()
checkBuffer()
[0,0]
buff_indx ++
startTimer()
Example Single node broadcast

## Slide 10
0
1
2
3
4
{}
{[0,0]}
{[0,0]}
{}
{}
event sendDone()
if(buff_indx > fwd_indx || carry != 0)
nothing to do!
Current state:
buff_indx = 1
fwd_indx = 1
carry = 0
Example Single node broadcast

## Slide 11
0
1
2
3
4
{}
{[0,0]}
{[0,0]}
{}
{}
<0,0>
event Timer.fired()
checkBuffer()
drop pkt
checkBuffer()
[0,0]
buff_indx ++
Example Single node broadcast
startTimer()

## Slide 12
0
1
2
3
4
{}
{[0,0]}
{[0,0]}
{[0,0]}
{}
event sendDone()
if(buff_indx > fwd_indx || carry != 0)
nothing to do!
Current state:
buff_indx = 1
fwd_indx = 1
carry = 0
Example Single node broadcast

## Slide 13
0
1
2
3
4
{}
{}
{}
{}
{}
<1,0>
checkBuffer()
[1,0]
buff_indx ++
startTimer()
Example Simultaneous node broadcast
(node of interest 2)
<3,0>
Current state:
buff_indx = 1
fwd_indx = 0
carry = 0

## Slide 14
0
1
2
3
4
{}
{}
{[1,0]}
{}
{}
<1,0>
checkBuffer()
[3,0]
buff_indx ++
startTimer()
<3,0>
Current state:
buff_indx = 2
fwd_indx = 0
carry = 0
already running
Example Simultaneous node broadcast
(node of interest 2)

## Slide 15
0
1
2
3
4
{}
{}
{[1,0],[3,0]}
{}
{}
<1,0>
event Timer.fired()
Current state:
buff_indx = 2
fwd_indx = 1
carry = 0
Example Simultaneous node broadcast
(node of interest 2)

## Slide 16
0
1
2
3
4
{}
{}
{}
{}
if(buff_indx > fwd_indx || carry != 0)
startTimer()
Current state:
buff_indx = 2
fwd_indx = 1
carry = 0
{[1,0],[3,0]}
event sendDone()
Example Simultaneous node broadcast
(node of interest 2)

## Slide 17
0
1
2
3
4
{}
{}
{[1,0],[3,0]}
{}
{}
<3,0>
event Timer.fired()
Current state:
buff_indx = 2
fwd_indx = 2
carry = 0
Example Simultaneous node broadcast
(node of interest 2)

## Slide 18
0
1
2
3
4
{}
{}
{}
{}
event sendDone()
if(buff_indx > fwd_indx || carry != 0)
nothing to do!
Current state:
buff_indx = 2
fwd_indx = 2
carry = 0
{[1,0],[3,0]}
Example Simultaneous node broadcast
(node of interest 2)

## Slide 19: Experiments
Topologies
No. nodes 9, 15 & 26 respectively to each of the below:
  Chain
  Tree
  Grid

## Slide 20: Tree
14 nodes
0
2
5
6
8
1
3
4
7
8 nodes
25 nodes
0
3
1
6
2
13
9
8
10
7
5
4
11
14
12
0
3
19
11
20
1
6
5
4
16
17
12
15
25
2
9
8
7
10
18
23
22
24
21
13
14

## Slide 21: Grid
14 nodes
8 nodes
25 nodes
0
1
2
3
4
5
6
7
8
0
1
2
4
5
6
11
9
10
3
7
8
12
13
14
0
1
2
5
6
7
10
11
12
3
8
13
4
9
14
15
16
17
20
21
22
18
23
19
24

## Slide 22: Conclusions
Chain:
  huge average and max latency
  bad coverage
Tree:
  good average latency
  better coverage than chain but still not the best
Grid:
  best average latency
  best coverage
  more duplicate/dropped packets (almost 2x of those in tree, chain)