## Slide 1: Wireless Sensor Networks
Assignment 5
Network-level application support
Μπαδάκης Ιωάννης 1590
Τσακίρης Τρύφων 1655

## Slide 2: Description
Development of a complete platform that supports deployment and execution of applications in WSN
Requirements:
  Long running queries
  Return of results back to the sink
  Removal of applications

## Slide 3: Design
Propagation
  Best-effort network-wide broadcast mechanism
Packet structure
  Broadcast Packet
    group id
    seq_no
    app
      app_id
      originator
      application binary
    * (originator, seq_no) define a unique application

## Slide 4: Design
Packet Structure(cont’d)
  Unicast Packet
    seq (binary sequence number, either 0 or 1, it’s used to distinguish different periods)
    reg7
    reg8
    originator
    app_id
    path_indx
    path[] (buffer to track the path of the packet, contains node ids)
  Termination Packet
    app_id
    originator

## Slide 5: Design
Buffering
  Whenever a node receives a new application, it starts executing it and floods it to the network while keeping some information about the sender
  Routing Table
    [ next_hop, originator]
  Application
    Lengths of different event handlers
      bin_len
      init_len
      timer_len
      msg_len

## Slide 6: Design
Application(cont’d)
  pc
  originator
  app_id
  seq
  application binary
  10 registers
    6: 1-byte general purpose
    4: 1-byte special purpose (incoming, outgoing application-level messages)
  flags
    waiting
    active
    received
    aggr_mode
    timer_fired

## Slide 7: Design
Queues
  HandlerQueue()
    contains received messages for the message handler
  SendQueue()
    contains all the “ready” messages to be sent

## Slide 8: Design
Tasks
  bufferMsg
    drop duplicate packets/apps
    save non-duplicates
    schedule a transmission time
  bufferResult
    handle received unicast messages
      execute interpeter for the msg_handler (if no event-handler is executing)
      either pass them to the HandlerQueue or send them transparently
    adjust aggregation back-off
  interpreter
    execute instructions 1-by-1 “pseudo concurrently” among all the active applications
    repost as long as there are more instructions to be executed

## Slide 9: Design
Tasks
  brodacastMsg
    broadcast the application
  forwardMsg
    forward the received application
  unicastMsg
    unicast the results of an application
  terminateMsg
    broadcast or unicast a termination message

## Slide 10: Design
Timers
  Each application has its own timer
  A single timer for caching techniques, to avoid an overly frequent sensor access
    CACHE_INTERVAL = 1000 msec

## Slide 11: Example App Propagation
0
1
2
3
4
{}
{}
{0}
{}
{}
{}
{}
{}
{}
{}
packet payload:
group_id = 4
seq_no = 0
app
  app_id = 0
  originator = 0
  app_bin
routing_table
apps_buffer

## Slide 12: Example App Propagation
0
1
2
3
4
{}
{0}
{[0,0]}
{}
{}
{}
{}
{}
{}
checkBuffer()
n
y
drop pkt
saveToBuffer()
startCollisionTimer()
saveApplication()
newRoutingTableEntry()
post interpreter
{0}

## Slide 13: Example App Propagation
0
1
2
3
4
{}
{0}
{[0,0]}
{0}
{[1,0]}
{0}
{[3,0]}
{0}
{[1,0]}
{0}

## Slide 14: Example App Propagation
0
1
2
3
4
{}
{0}
{[0,0]}
{0}
{[1,0]}
{0}
{[3,0]}
{0}
{[1,0]}
{0}
packet payload:
seq = 0
reg7 = 34
reg8 = 0
originator = 0
app_id = 0
path_indx = 1
path = [4]
event App0Timer.fired()

## Slide 15: Example App Propagation
0
1
2
3
4
{}
{0}
{[0,0]}
{0}
{[1,0]}
{0}
{[3,0]}
{0}
{[1,0]}
{0}
packet payload:
seq = 0
reg7 = 34
reg8 = 0
originator = 0
app_id = 0
path_indx = 2
path = [4,3]
event App0Timer.fired()
Likewise for the other nodes

## Slide 16: Example App Termination
0
1
2
3
4
{}
{0}
{[0,0]}
{0}
{[1,0]}
{0}
{[3,0]}
{0}
{[1,0]}
{0}
packet payload:
app_id
originator

## Slide 17: Example App Termination
0
1
2
3
4
{}
{}
{[0,0]}
{0}
{[1,0]}
{0}
{[3,0]}
{0}
{[1,0]}
{}
packet payload:
app_id
originator

## Slide 18: Example App Termination
0
1
2
3
4
{}
{}
{[0,0]}
{}
{[1,0]}
{0}
{[3,0]}
{0}
{[1,0]}
{}
packet payload:
app_id
originator
lost packet

## Slide 19: Example App Termination
0
1
2
3
4
{}
{}
{[0,0]}
{}
{[1,0]}
{}
{[3,0]}
{0}
{[1,0]}
{}
children = 0
no need to broadcast termination msg

## Slide 20: Example App Termination
0
1
2
3
4
{0}
{[1,0]}
packet payload:
unicast msg
{}
{[0,0]}
{}
{[1,0]}
{[3,0]}
{}
{}
{}
event App0Timer.fired()

## Slide 21: Example App Termination
0
1
2
3
4
{0}
{[1,0]}
{}
{[0,0]}
{}
{[1,0]}
{[3,0]}
{}
{}
{}
isAppActive()
n
send termination msg with unicast

## Slide 22: Example App Termination
0
1
2
3
4
{0}
{[1,0]}
{}
{[0,0]}
{}
{[1,0]}
{[3,0]}
{}
{}
{}
packet payload:
app_id
originator

## Slide 23: Example App Termination
0
1
2
3
4
{}
{[1,0]}
{}
{[0,0]}
{}
{[1,0]}
{[3,0]}
{}
{}
{}
children = 0
no need to broadcast termination msg